## Slide 1: Ansys Automation
Michael Quach
DiTTA - ARO
October 13th, 2023

## Slide 2: Introduction
Programming Essentials
Ansys Design Modeler API
Ansys Mechanical API
References
Courtesy:
Ansys

## Slide 3: Programming Essentials
GitHub
  GitHub is a data repository and management tool for software development
  Folders are categorized for their specific purpose
JavaScript
  Ansys Design Modeler uses JavaScript to automatically populate the workspace with a previous constructed model
  Allows the user the ability to save their sketches as a Javas Script
Python
  Ansys Mechanical uses Python to automate the simulation and exporting the results

## Slide 4: For Demonstration Purposes Only
Ansys DesignModeler
(JavaScript)
Utilize the project files in “Simulation” Folder as a starter

## Slide 5: Ansys DesignModeler Essentials
Key Objects
  agb: Points to the batch interface
  p: Plane sketches object for whole model
Key Functions
  HorizontalDim and VerticalDim
  HoriztonalCon, VerticalCon, CoincidentCon
Key Properties and Methods
  p.Sk: Specific sketch of the model
  p.Ln(): Dimensions of the model
  agb.regen(): Regenerates the workspace
  agb.Extrude(): Extrudes a specific sketch based on given parameters

## Slide 6: Top Portion of Script
beamModel_Inches.js

## Slide 7: Ansys Design Modeler
Right-click on
“Geometry”
Right-click on
“Edit Geometry in DesignModeler”

## Slide 8: Setting-up the Model (DesignModeler)
Click on
“File -> Run Script”
Select JavaScript file based on desired units
Automatically produces beam with damaged cuts

## Slide 9
Ansys Mechanical
(Python)

## Slide 10: Key Methods and Properties
Key Objects
  DataModel: Main object that houses all the sub-objects, methods, and properties
Key Properties and Methods
  .Solution: Sets up the solution
  .Activate(): Activates the solution object within the workspace
  .AddTotalDeformation(): One of the various methods provided to add a desired result/analysis
  .Solve(True): Solves for all the desired results
  .ExportToTextFile(filePath): Exports all the results for the nodes to individual text files

## Slide 11: Top Portion of Script
solutionsAndExport.py

## Slide 12: Setting-up Analysis (Mechanical)
Click on
“Model -> Edit…”
Load scenario with forces already set-up
Click-on
“Automation -> Scripting”

## Slide 13: Mechanical Scripting Loading
Click on the
“Folder”
Click on
“solutionsAndExport.py”
Select loads into the IDE

## Slide 14: Running the script and solutions
Click on the
“Play button”
Identifies where the files are saves
View the results of the analysis

## Slide 15: Example Output
Text file containing the results

## Slide 16: Compiling results
resultsCompiler.m
Text file containing the results
resultsComplier.m

## Slide 17: Example of Compiled Results

## Slide 18: References

## Slide 19
Thank you!